## Slide 1
Case basis and data interpretation
Inputs drawn from the component reference, case-data sheet, and calculation template.
Process basis | Specified value
Column configuration | Total condenser; kettle reboiler
Operating pressure | 7.0 bar
Feed rate | 24,000 kg/h
Feed mass fractions | CH4 = 0.62; C2H4 = 0.38
Feed thermal condition | Subcooled; q = 1.2
Relative volatility | alpha_top = 2.500; alpha_bottom = 1.369; alpha_eff = 1.850
Product basis | Value
GC vapor ratio | CH4 : C2H4 = 18.0 : 1.00
Distillate mole fractions | xD,CH4 = 0.9474; xD,C2H4 = 0.0526
Bottoms mole fractions | xB,CH4 = 0.0100; xB,C2H4 = 0.9900
Key assignment | LK = methane; HK = ethene
Interpretation used in the validation
The vapor-line GC ratio is normalized directly as the distillate composition. The shortcut stage estimate counts the kettle reboiler as an equilibrium stage and excludes the total condenser.
CH4 / C2H4 splitter shortcut validation

## Slide 2
Shortcut calculation approach
Three linked calculations convert the supplied basis into the reflux and stage estimates.
Fenske
Minimum stages at total reflux
Uses light-key/heavy-key product split and constant alpha to compute Nmin.
Underwood
Minimum reflux from q-line root
Solves the root between alpha_HK = 1.000 and the effective alpha_LK (Section 1 geometric mean), then computes Rmin.
Gilliland
Operating stage estimate
Uses R = 1.25 x Rmin and the Eduljee explicit form for the continuous N estimate.
Verification discipline
Full-precision theta and Rmin are used for Underwood back-substitution before final values are rounded.
Reporting basis
Theta, Rmin, R, mole fractions, D/F, and B/F are shown to four decimals; Nmin and N are shown to two decimals.
CH4 / C2H4 splitter shortcut validation

## Slide 3
Principal shortcut results
The operating case uses R = 1.25 x Rmin and returns a continuous theoretical stage estimate.
1.1243
Underwood root theta
Selected root: 1 < theta < alpha_eff
0.9918
Minimum reflux ratio Rmin
Rmin + 1 = 1.9918
1.2397
Operating reflux ratio R
1.25 x Rmin
27.29
Gilliland / Eduljee N
Continuous theoretical stages
Calculated item | Result | Basis
Minimum stages, Nmin | 12.17 | Includes kettle reboiler; excludes total condenser
Operating stage estimate, N | 27.29 | Eduljee/Gilliland at R = 1.2397
D/F, molar basis | 0.7793 | From CH4 component balance
B/F, molar basis | 0.2207 | 1 - D/F
CH4 / C2H4 splitter shortcut validation

## Slide 4
Molar-balance closure
The normalized product compositions close the overall and component balances on a molar basis.
0.7793
Distillate fraction D/F
Molar product split
0.2207
Bottoms fraction B/F
Molar product split
1.0000
Overall closure
D/F + B/F
Component check | Calculated value | Feed target
CH4: (D/F)xD,CH4 + (B/F)xB,CH4 | 0.7405 | zCH4 = 0.7405
C2H4: (D/F)xD,C2H4 + (B/F)xB,C2H4 | 0.2595 | zC2H4 = 0.2595
Balance implication: the GC-derived distillate composition and specified bottoms composition produce a consistent product split for the shortcut validation.
CH4 / C2H4 splitter shortcut validation

## Slide 5
Engineering implications and limitations
Use the shortcut results as a traceable validation package, not as a substitute for detailed design.
27.29
Theoretical stage estimate
Continuous equilibrium stages at R = 1.2397
12.17
Minimum basis
Nmin at total reflux
1.25 x Rmin
Reflux basis
Specified operating trade-off
Board takeaway | Why it matters
Shortcut package is internally consistent | Fenske, Underwood, Eduljee, and molar balances produce one coherent calculation basis.
Do not overstate original design acceptance | The starter data do not provide the actual tray count, efficiency, hydraulics, or pressure profile.
Most important sensitivities | Constant relative volatility, q = 1.2, and the vapor-GC interpretation should be checked before final design lock.
CH4 / C2H4 splitter shortcut validation